library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

------------------------------------------------------------------------------------
--Title: MemoryGame
--Name: Nathaniel Roberts, Mitch Walker
--Date: 4/23/25
--Prof: Scott Tippens
--Desc: Memory Game design file
-- This module contains the main operating instructions of the Memory game.
--
-- To start the game a player must press the center push button.
-- Then 5 separate leds will light on the 16 wide led display once each second.
--
-- They player must recall the order of the leds by flipping the corresponding
-- slide switch. Once all numbers were guessed correctly, a short victory patter
-- lights, the score increments and the next round starts automatically.
--
-- Each successive round is faster than the last. The game ends at any point the
-- player guesses the wrong number during their turn.
------------------------------------------------------------------------------------

entity MemoryGame is
    generic(
        MAX_COUNT_SCALER : integer;
        SCALE_AMOUNT : integer;
        MAX_TOGGLE_COUNT : integer;
        BLINK_COUNT : integer
    );
    port(
        switches : in std_logic_vector(15 downto 0);
        start : in std_logic;

        clock : in std_logic;
        reset : in std_logic;

        leds : out std_logic_vector(15 downto 0);

        outputScore : out std_logic_vector(7 downto 0);

        blanks : out std_logic_vector(3 downto 0)
    );
end entity MemoryGame;

architecture MemoryGame_ARCH of MemoryGame is

    ------------------------------------------------------------------------------------
    --constants and status signals
    ------------------------------------------------------------------------------------

    --this is subtracted from the toggling counter, making the leds blink faster
    signal countScaler : integer range 0 to MAX_COUNT_SCALER;

    ------------------------------------------------------------------------------------
    --component definitions
    ------------------------------------------------------------------------------------
    component RandomNumbers is
        port(
        generateEN : in std_logic;
        clock : in std_logic;
        reset : in std_logic;

        readyEN : out std_logic;

        number0 : out std_logic_vector(3 downto 0);
        number1 : out std_logic_vector(3 downto 0);
        number2 : out std_logic_vector(3 downto 0);
        number3 : out std_logic_vector(3 downto 0);
        number4 : out std_logic_vector(3 downto 0)
        );
    end component RandomNumbers;

    component NumberChecker is
        port(
        switches : in std_logic_vector(15 downto 0);

        number0 : in std_logic_vector(3 downto 0);
        number1 : in std_logic_vector(3 downto 0);
        number2 : in std_logic_vector(3 downto 0);
        number3 : in std_logic_vector(3 downto 0);
        number4 : in std_logic_vector(3 downto 0);

        readMode : in std_logic;

        clock : in std_logic;
        reset : in std_logic;

        gameOverEN : out std_logic;
        gameWinEN : out std_logic
        );
    end component NumberChecker;

    component WinPattern
        generic(BLINK_COUNT : natural);
        port(
        winPatternMode : in std_logic;
        reset : in std_logic;
        clock : in std_logic;
        leds : out std_logic_vector(15 downto 0)
        );
    end component WinPattern;

    component LosePattern
        generic(BLINK_COUNT : natural);
        port(
        losePatternEN : in std_logic;
        reset : in std_logic;
        clock : in std_logic;
        leds : out std_logic_vector(15 downto 0);
        losePatternIsBusy : out std_logic
        );
    end component LosePattern;

    component LedSegments
        port(
        binary4Bit : in std_logic_vector(3 downto 0);
        outputMode : in std_logic;
        leds : out std_logic_vector(15 downto 0)
        );
    end component LedSegments;

    component BCD
        port(
        binary4Bit : in std_logic_vector(3 downto 0);
        decimalOnes : out std_logic_vector(3 downto 0);
        decimalTens : out std_logic_vector(3 downto 0)
        );
    end component BCD;

    ------------------------------------------------------------------------------------
    -- connecting signals
    ------------------------------------------------------------------------------------
    --Signals for RNG_GENERATOR
    signal readyEN : std_logic;
    signal number0 : std_logic_vector(3 downto 0);
    signal number1 : std_logic_vector(3 downto 0);
    signal number2 : std_logic_vector(3 downto 0);
    signal number3 : std_logic_vector(3 downto 0);
    signal number4 : std_logic_vector(3 downto 0);
    signal outputNumber : std_logic_vector(3 downto 0);

    --Control signal for the RNG_GENERATOR
    signal startControl : std_logic;

    --Signals for CHECK_NUMBERS
    signal readMode : std_logic;
    signal nextRoundEN : std_logic;
    signal gameOverEN : std_logic;
    signal gameWinEN : std_logic;
    signal ledMode : std_logic;

    --Score represented as a integer and later converted to vector
    signal score : integer range 0 to 15;
    signal scoreVector : std_logic_vector(3 downto 0);

    --Level signal to make sure user cannot press the start button
    --while the lose pattern is playing.
    signal losePatternIsBusy : std_logic;

    --Timer controlled state signal
    signal SMTimer : integer;

    --Level controls for the win and lose patters
    signal loseMode : std_logic;
    signal winMode : std_logic;

begin

    ------------------------------------------------------------------------------------
    -- Random number generator component controlled by a combinational control signal
    ------------------------------------------------------------------------------------
    startControl <= (start and readMode and (not losePatternIsBusy)) or nextRoundEN;
    RNG_GENERATOR : component RandomNumbers port map(
        generateEN => startControl,

        clock => clock,
        reset => reset,

        --------------outputs
        readyEN => readyEN,

        number0 => number0,
        number1 => number1,
        number2 => number2,
        number3 => number3,
        number4 => number4
    );

    ------------------------------------------------------------------------------------
    -- Number checker component that ouputs a pulse when all numbers intered are correct
    ------------------------------------------------------------------------------------
    CHECK_NUMBERS : component NumberChecker port map(
        switches => switches,

        number0 => number0,
        number1 => number1,
        number2 => number2,
        number3 => number3,
        number4 => number4,

        readMode => readMode,

        clock => clock,
        reset => reset,

        --------------outputs
        gameOverEN => gameOverEN,
        gameWinEN => gameWinEN
    );

    ------------------------------------------------------------------------------------
    -- Win pattern generator that is mode controlled, outpus a pulse to start next round
    ------------------------------------------------------------------------------------
    WIN_PATTERN_DRIVER : component WinPattern
        generic map(
        BLINK_COUNT => BLINK_COUNT
        )
        port map(
        winPatternMode => winMode,
        reset => reset,
        clock => clock,

        --------------outputs
        leds => leds
    );

    ------------------------------------------------------------------------------------
    -- Lose pattern generator that is pulse controlled,
    -- ouputs a level control high if it is activley controlling the leds.
    ------------------------------------------------------------------------------------
    LOSE_PATTERN_DRRIVER : LosePattern
        generic map(
        BLINK_COUNT => BLINK_COUNT
        )
        port map(
        losePatternEN => gameOverEN,
        reset => reset,
        clock => clock,

        --------------outputs
        leds => leds,
        losePatternIsBusy => losePatternIsBusy
    );

    ------------------------------------------------------------------------------------
    -- Takes a 4 bit binary word and converts to a positional 16 bit wide vector for leds.
    -- This component drives all leds to Z if the outputMode port is low.
    ------------------------------------------------------------------------------------
    GAME_LED_DRIVER : LedSegments port map(
        binary4Bit => outputNumber,
        outputMode => ledMode, --if outputMode is low, then this output is (others => 'Z')

        --------------outputs
        leds => leds
    );

    ------------------------------------------------------------------------------------
    -- Code conversion component to change a binary number to BCD
    ------------------------------------------------------------------------------------
    scoreVector <= std_logic_vector(to_unsigned(score, 4));
    SCORE_NUMBER_BCD : BCD port map(
        binary4Bit => scoreVector,

        --------------outputs
        decimalOnes => outputScore(3 downto 0),
        decimalTens => outputScore(7 downto 4)
    );

    ------------------------------------------------------------------------------------
    -- Process that increments score and speed with each win.
    -- Whenever the gameOverEN signal pulses, the loseMode latch is set, which activates
    -- the LOSE_MODE_TIMER process.
    ------------------------------------------------------------------------------------
    GAME_DRIVER : process (clock, reset)
    begin
        if reset = '1' then
        score <= 0;
        countScaler <= 0;
        loseMode <= '0';
        elsif rising_edge(clock) then
        if gameWinEN = '1' then
        score <= score + 1;
        if countScaler <= MAX_COUNT_SCALER - 1 then
        countScaler <= countScaler + SCALE_AMOUNT;
        end if;
        end if;
        if gameOverEN = '1' then
        countScaler <= 0;
        loseMode <= '1';
        end if;
        end if;
    end process;

    ------------------------------------------------------------------------------------
    -- Timer that handles blinking the final score until reset happens.
    -- This process can only run the LosePattern module if loseMode was set by GAME_DRIVER.
    ------------------------------------------------------------------------------------
    LOSE_MODE_TIMER : process(clock, reset)
        variable counter : integer range 0 to MAX_TOGGLE_COUNT - 1;
        variable toggle : std_logic;
    begin
        if reset = '1' then
        counter := 0;
        toggle := '0';
        elsif rising_edge(clock) then
        if loseMode = '1' then
        counter := counter + 1;
        if (counter >= (MAX_TOGGLE_COUNT - 1)) then
        toggle := not toggle;
        counter := 0;
        end if;
        if toggle = '1' then
        blanks <= "0011";
        elsif toggle = '0' then
        blanks <= "1111";
        end if;

        elsif loseMode = '0' then
        counter := 0;
        blanks <= "0011";
        end if;
        end if;
    end process;

    ------------------------------------------------------------------------------------
    --Timer that handles automatic start and level controlled win pattern.
    ------------------------------------------------------------------------------------
    WIN_MODE_TIMER : process(clock, reset)
        variable counter : integer range 0 to (2 * MAX_TOGGLE_COUNT) - 1;
        variable latch : std_logic;
        variable godMode : std_logic;
    begin
        if reset = '1' then
        counter := 0;
        latch := '0';
        nextRoundEN <= '0';
        godMode := '0';
        elsif rising_edge(clock) then

        --Once the number checker component sends the gameWinEN pulse
        --then the latch variable goes high. Same for the godMode latch.
        nextRoundEN <= '0';
        if gameWinEN = '1' then
        latch := '1';
        elsif score = 15 then
        godMode := '1';
        end if;

        --Depending if one latch or another was set, then then
        --mode controlled WinPattern component takes over the leds.
        if godMode = '1' then
        winMode <= '1';
        elsif latch = '1' then
        winMode <= '1';
        counter := counter + 1;
        if (counter >= ((2 * MAX_TOGGLE_COUNT) - 1)) then
        latch := '0';
        counter := 0;
        nextRoundEN <= '1';
        end if;
        elsif latch = '0' then
        counter := 0;
        winMode <= '0';
        else
        counter := 0;
        winMode <= '0';
        end if;
        end if;
    end process;

    ------------------------------------------------------------------------------------
    --Timer that directs the display the values of RNG_GENERATOR.
    ------------------------------------------------------------------------------------
    DISPLAY_SM_TIMER : process(clock,reset)
        variable counter : integer range 0 to MAX_TOGGLE_COUNT - 1;
        variable countMode : std_logic;
    begin
        if reset = '1' then
        SMTimer <= 0;
        counter := 0;
        countMode := '0';
        elsif rising_edge(clock) then

        --The readyEN pulse from the RNG_GENERATOR component will latch this
        --internal variable high, enabling the next if statement.
        if readyEN = '1' then
        countMode := '1'; --latch in and start counting
        end if;

        --The counter variable reaches it's terminal value once each second.
        --Each time the terminal value is reached, the SMTimer signal increments.
        --After reaching that terminal value 9 times, it goes back to a steady state.
        if countMode = '1' then
        counter := counter + 1;
        if (counter >= (MAX_TOGGLE_COUNT - countScaler - 1)) then
        SMTimer <= SMTimer + 1;
        counter := 0;
        end if;
        elsif countMode = '0' then
        SMTimer <= 0;
        counter := 0;
        end if;

        if SMTimer = 10 then
        SMTimer <= 0;
        countMode := '0';
        counter := 0;
        end if;
        end if;
    end process;

    ------------------------------------------------------------------------------------
    -- State machine responsible for multiplexing the random number to leds
    -- in addition to writing control signals.
    -- This state machine was designed this way to cut down dignificantly on the
    -- unintentional latches of previous display state machine designs.
    ------------------------------------------------------------------------------------
    DISPLAY_SM : process(SMTimer, number0, number1, number2, number3, number4, loseMode) is
    begin
        case (SMTimer) is
        ------------------------------------------------------------------BLANK
        when 0 =>
        readMode <= '1'; --allow the start button to be pressed
        ledMode <= '0'; --deactivate LedSegments component

        ------------------------------------------------------------------NUM1
        when 1 =>
        readMode <= '0';
        ledMode <= '1'; --activate LedSegments component
        outputNumber <= number0;

        ------------------------------------------------------------------BLANK
        when 2 =>
        readMode <= '0';
        ledMode <= '0'; --deactivate LedSegments component

        ------------------------------------------------------------------NUM2
        when 3 =>
        readMode <= '0';
        ledMode <= '1'; --activate LedSegments component
        outputNumber <= number1;

        ------------------------------------------------------------------BLANK
        when 4 =>
        readMode <= '0';
        ledMode <= '0'; --deactivate LedSegments component

        ------------------------------------------------------------------NUM3
        when 5 =>
        readMode <= '0';
        ledMode <= '1'; --activate LedSegments component
        outputNumber <= number2;

        ------------------------------------------------------------------BLANK
        when 6 =>
        readMode <= '0';
        ledMode <= '0'; --deactivate LedSegments component

        ------------------------------------------------------------------NUM4
        when 7 =>
        readMode <= '0';
        ledMode <= '1'; --activate LedSegments component
        outputNumber <= number3;

        ------------------------------------------------------------------BLANK
        when 8 =>
        readMode <= '0';
        ledMode <= '0'; --deactivate LedSegments component

        ------------------------------------------------------------------NUM5
        when 9 =>
        readMode <= '0';
        ledMode <= '1'; --activate LedSegments component
        outputNumber <= number4;

        ----------------------------------------------------------DEFAULT case
        when others =>
        readMode <= '0';
        ledMode <= '0'; --deactivate LedSegments component

        end case;

    end process;

end architecture MemoryGame_ARCH;

library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;

----------------------------------------------------------------------------------
--Title: RandomNumbers.vhd
--Name: Nathaniel Roberts, Mitch Walker
--Date: 3/26/25
--Prof: Scott Tippens

-- Description: Random Number Generator
-- This component utilizes 5 counters incrementing at different rates to
-- generate 5 psuedo-random numbers
--
-- Each RandCounter has a sub counter. Once the sub counter reaches its
-- max value (set externally through maxSubCount) the randNum counter is
-- incremented
--
-- Once generateEN recieves a pulse, SET_RAND_NUM sets the output signals
-- to their corresponding randNum counter value. SET_RAND_NUM them sends
-- a pulsed signal through readyEN to signify that new random numbers
-- have been set
-- Dependencies: RandCounter.vhd
----------------------------------------------------------------------------------

entity RandomNumbers is
    port (
        generateEN : in std_logic;
        clock : in std_logic;
        reset : in std_logic;

        readyEN : out std_logic;
        number0 : out std_logic_vector(3 downto 0);
        number1 : out std_logic_vector(3 downto 0);
        number2 : out std_logic_vector(3 downto 0);
        number3 : out std_logic_vector(3 downto 0);
        number4 : out std_logic_vector(3 downto 0)
    );
end RandomNumbers;

architecture RandomNumbers_ARCH of RandomNumbers is
    ---------------------------------------------------------------------------------
    -- Constants
    ---------------------------------------------------------------------------------
    constant ACTIVE : std_logic := '1'; -- Active value
    constant COUNTER_MAX_VALUE : integer := 15; -- Max value for 'random' counters
    constant maxSubCount_Length : integer := 3; -- Length of the subCount signal within RandCounter component

    constant MAX_SUB_COUNT_0 : integer := 3; -- Max value for sub counter 1
    constant MAX_SUB_COUNT_1 : integer := 1; -- Max value for sub counter 2
    constant MAX_SUB_COUNT_2 : integer := 2; -- Max value for sub counter 3
    constant MAX_SUB_COUNT_3 : integer := 5; -- Max value for sub counter 4
    constant MAX_SUB_COUNT_4 : integer := 4; -- Max value for sub counter 5

    ----------------------------------------------------------------------------------
    -- Components
    ----------------------------------------------------------------------------------
    component RandCounter is
        port (
        maxSubCount : in std_logic_vector(2 downto 0);
        clock : in std_logic;
        reset : in std_logic;

        randNum : out std_logic_vector(3 downto 0)
        );
    end component;
    ----------------------------------------------------------------------------------
    -- Signals
    ----------------------------------------------------------------------------------
    signal randNum0 : std_logic_vector(3 downto 0);
    signal randNum1 : std_logic_vector(3 downto 0);
    signal randNum2 : std_logic_vector(3 downto 0);
    signal randNum3 : std_logic_vector(3 downto 0);
    signal randNum4 : std_logic_vector(3 downto 0);

begin

    ---------------------------------------------------------------------------------
    -- Component Instatiations
    ---------------------------------------------------------------------------------
    -- Used to generate pseudo-random value for randNum0
    RAND_COUNTER_0 : RandCounter port map (
      maxSubCount => std_logic_vector(to_unsigned(MAX_SUB_COUNT_0, maxSubCount_Length)),
      clock => clock,
      reset => reset,
      randNum => randNum0
    );

    RAND_COUNTER_1 : RandCounter port map (
      maxSubCount => std_logic_vector(to_unsigned(MAX_SUB_COUNT_1, maxSubCount_Length)),
      clock => clock,
      reset => reset,
      randNum => randNum1
    );

    RAND_COUNTER_2 : RandCounter port map (
      maxSubCount => std_logic_vector(to_unsigned(MAX_SUB_COUNT_2, maxSubCount_Length)),
      clock => clock,
      reset => reset,
      randNum => randNum2
    );

    RAND_COUNTER_3 : RandCounter port map (
      maxSubCount => std_logic_vector(to_unsigned(MAX_SUB_COUNT_3, maxSubCount_Length)),
      clock => clock,
      reset => reset,
      randNum => randNum3
    );

    RAND_COUNTER_4 : RandCounter port map (
      maxSubCount => std_logic_vector(to_unsigned(MAX_SUB_COUNT_4, maxSubCount_Length)),
      clock => clock,
      reset => reset,
      randNum => randNum4
    );

    ---------------------------------------------------------------------------------
    -- Checks for generateEN signal
    -- Sets the output numbers to the current values of their respective counters
    -- Outputs a pule through readyEN
    ---------------------------------------------------------------------------------
    SET_RAND_NUM : process(clock, reset)
        variable newNumSet : std_logic := not ACTIVE;
    begin
        if reset = ACTIVE then
        readyEN <= not ACTIVE;
        newNumSet := not ACTIVE;

        number0 <= "0000";
        number1 <= "0000";
        number2 <= "0000";
        number3 <= "0000";
        number4 <= "0000";
        elsif rising_edge(clock) then
        if generateEN = ACTIVE then
        number0 <= randNum0;
        number1 <= randNum1;
        number2 <= randNum2;
        number3 <= randNum3;
        number4 <= randNum4;
        newNumSet := ACTIVE;
        end if;

        if newNumSet = ACTIVE then
        readyEN <= ACTIVE;
        newNumSet := not ACTIVE;
        else
        readyEN <= not ACTIVE;
        end if;
        end if;
    end process;

end RandomNumbers_ARCH;

library IEEE;
use IEEE.STD_LOGIC_1164.ALL;
use IEEE.NUMERIC_STD.ALL;

------------------------------------------------------------------------------------
--Title: RandCounter.vhd
--Name: Nathaniel Roberts, Mitch Walker
--Date: 3/26/25
--Prof: Scott Tippens
--Desc: Each clock cycle, cubCount increments by 1
-- Once subCount surpasses maxSubCount, subCount is reset to 0,
-- and randNum is incremented by 1.
--
-- Once randNum surpasses 15, randNum is reset to 0
------------------------------------------------------------------------------------

entity RandCounter is
    Port (
        ------------ Inputs
        maxSubCount : in std_logic_vector(2 downto 0);
        clock : in std_logic;
        reset : in std_logic;

        ------------ Outputs
        randNum : out std_logic_vector(3 downto 0)
    );
end RandCounter;

architecture RandCounter_ARCH of RandCounter is
    constant ACTIVE : std_logic := '1';
    constant MAX_COUNT : integer := 15;
begin

    Counter : process(clock, reset)
        -- Counters used to generate pseudo-random number
        variable subCount : integer := 0;
        variable count : integer := 0;
    begin
        if reset = ACTIVE then
        subCount := 0;
        count := 0;
        randNum <= "0000";
        elsif rising_edge(clock) then
        -- Checks if subcount has surpassed maxSubCount
        if subCount < to_integer(unsigned(maxSubCount)) then
        subCount := subCount + 1;
        else
        subCount := 0;
        count := count + 1;
        end if;

        -- Checks if count has surpassed MAX_COUNT
        if count > MAX_COUNT then
        count := 0;
        end if;

        -- Assigns the count to randNum as a std_logic_vector
        randNum <= std_logic_vector(to_unsigned(count, randNum'length));
        end if;
    end process;
end RandCounter_ARCH;

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
------------------------------------------------------------------------------------
--Title: NumberChecker
--Name: Nathaniel Roberts, Mitch Walker
--Date: 4/23/25
--Prof: Scott Tippens
--Desc: Number Checker component
-- The component will output a pulse on one of three pins to indicate if
-- the user made all the correct entries or made an error.

-- When there are 5 numbers to check, the gameWinEN gets a pulse
-- if all are entered correctly.

-- At any point a wrong number is made, gameOverEN gets a pulse.
------------------------------------------------------------------------------------
entity NumberChecker is
    port(
        switches : in std_logic_vector(15 downto 0); --the pulsed switch inputs go here

        number0 : in std_logic_vector(3 downto 0);
        number1 : in std_logic_vector(3 downto 0);
        number2 : in std_logic_vector(3 downto 0);
        number3 : in std_logic_vector(3 downto 0);
        number4 : in std_logic_vector(3 downto 0);

        readMode : in std_logic; -- pull this port low when the display is used

        clock : in std_logic;
        reset : in std_logic;

        gameOverEN : out std_logic;
        gameWinEN : out std_logic
    );
end entity NumberChecker;

architecture NumberChecker_ARCH of NumberChecker is
    signal compare : integer range 0 to 16;

    signal num0 : integer range 0 to 16;
    signal num1 : integer range 0 to 16;
    signal num2 : integer range 0 to 16;
    signal num3 : integer range 0 to 16;
    signal num4 : integer range 0 to 16;

    signal progressCounter : natural range 1 to 5;

begin

    with switches select
        compare <= 1 when "0000000000000001",
        2 when "0000000000000010",
        3 when "0000000000000100",
        4 when "0000000000001000",
        5 when "0000000000010000",
        6 when "0000000000100000",
        7 when "0000000001000000",
        8 when "0000000010000000",
        9 when "0000000100000000",
        10 when "0000001000000000",
        11 when "0000010000000000",
        12 when "0000100000000000",
        13 when "0001000000000000",
        14 when "0010000000000000",
        15 when "0100000000000000",
        16 when "1000000000000000",
        0 when others;

    num0 <= to_integer(unsigned(number0)) + 1;
    num1 <= to_integer(unsigned(number1)) + 1;
    num2 <= to_integer(unsigned(number2)) + 1;
    num3 <= to_integer(unsigned(number3)) + 1;
    num4 <= to_integer(unsigned(number4)) + 1;

    ------------------------------------------------------------------------------------
    -- Main number checker process:
    -- procressCounter keeps track of which number needs to be checked
    -- Each if statement will exit by pulling gameOverEN low if the numx mismatches compare
    -- Inputs are ignored if no switches are active during any rising_edge()
    ------------------------------------------------------------------------------------
    CHECK_NUMBERS : process(clock, reset)
    begin
        if reset = '1' then
        gameOverEN <= '0';
        gameWinEN <= '0';
        progressCounter <= 1;
        elsif rising_edge(clock) then
        gameOverEN <= '0';
        gameWinEN <= '0';

        if (readMode = '1') and (to_integer(unsigned(switches)) > 0) then

        if progressCounter = 1 then
        if compare = num0 then
        progressCounter <= progressCounter + 1;
        else
        gameOverEN <= '1';
        progressCounter <= 1;
        end if;
        elsif progressCounter = 2 then
        if compare = num1 then
        progressCounter <= progressCounter + 1;
        else
        gameOverEN <= '1';
        progressCounter <= 1;
        end if;
        elsif progressCounter = 3 then
        if compare = num2 then
        progressCounter <= progressCounter + 1;
        else
        gameOverEN <= '1';
        progressCounter <= 1;
        end if;
        elsif progressCounter = 4 then
        if compare = num3 then
        progressCounter <= progressCounter + 1;
        else
        gameOverEN <= '1';
        progressCounter <= 1;
        end if;
        elsif progressCounter = 5 then
        if compare = num4 then
        gameWinEN <= '1';
        progressCounter <= 1;
        else
        gameOverEN <= '1';
        progressCounter <= 1;
        end if;
        end if;
        end if;
        end if;
   end process;
end architecture NumberChecker_ARCH;
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

------------------------------------------------------------------------------------
--Title: WinPattern.vhd
--Name: Nathaniel Roberts, Mitch Walker
--Date:
--Prof: Scott Tippens
--Desc: Win pattern generator
-- This module handles drawing a specific win patternt to the 16 leds.
--
-- When inactive, the leds are put into high impedace to avoid multiple driven nets
--
------------------------------------------------------------------------------------

entity WinPattern is
    generic(BLINK_COUNT : natural); --(100000000/4)-1;
    port(
        winPatternMode : in std_logic;

        reset: in std_logic;
        clock: in std_logic;

        leds: out std_logic_vector(15 downto 0)
    );
end WinPattern;

architecture WinPattern_ARCH of WinPattern is

    constant ACTIVE: std_logic := '1';

    constant BLANK_LEDS : std_logic_vector(15 downto 0) := "ZZZZZZZZZZZZZZZZ";
    constant PATTERN0_LEDS : std_logic_vector(15 downto 0) := "1010101010101010";
    constant PATTERN1_LEDS : std_logic_vector(15 downto 0) := "0101010101010101";

    signal displayMode : std_logic;
    signal toggle : std_logic;

begin

    ------------------------------------------------------------------------------------
    -- The if this module's WinPatternMode port is high then it will begin displaying
    -- a shifing patter of leds. The toggle signal flips back and fourth between
    -- selecting one pattern or another. If this componenent is not selected, then
    -- the output is in high impedance.
    ------------------------------------------------------------------------------------
    WIN_SHIFT : process(clock, reset)
    begin
        if reset = '1' then
        leds <= BLANK_LEDS;
        elsif rising_edge(clock) then
        if winPatternMode = '1' then
        if toggle = '1' then
        leds <= PATTERN0_LEDS;
        elsif toggle = '0' then
        leds <= PATTERN1_LEDS;
        end if;
        else
        leds <= BLANK_LEDS;
        end if;
        end if;
    end process;

    ------------------------------------------------------------------------------------
    -- This process handles how fast the toggle signal fill flip back and fourth.
    ------------------------------------------------------------------------------------
    DISPLAY_RATE: process(reset, clock)
        variable count: integer range 0 to BLINK_COUNT;
    begin
        if (reset = ACTIVE) then
        count := 0;
        toggle <= not ACTIVE;
        elsif (rising_edge(clock)) then
        if winPatternMode = '1' then
        if (count >= BLINK_COUNT) then
        count := 0;
        toggle <= not toggle;
        else
        count := count + 1;
        end if;
        else
        count := 0;
        toggle <= not ACTIVE;
        end if;
        end if;
    end process DISPLAY_RATE;

end WinPattern_ARCH;

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

------------------------------------------------------------------------------------
--Title: LosePattern.vhd
--Name: Nathaniel Roberts, Mitch Walker
--Date:
--Prof: Scott Tippens
--Desc: Lose Pattern generator
-- And overly complex desin in code to essentially display a draining health bar.
--
-- Each pattern that is ouput to the leds is represented by a custom state.
--
-- The state machine of this file switches through all 16 patterns at the rate of
-- once every 1/4 second
------------------------------------------------------------------------------------

entity LosePattern is
    generic(BLINK_COUNT : natural);
    port(

        losePatternEN : in std_logic;

        reset: in std_logic;
        clock: in std_logic;

        leds: out std_logic_vector(15 downto 0);

        losePatternIsBusy : out std_logic
    );
end LosePattern;

architecture LosePattern_ARCH of LosePattern is

    type States_t is (BLANK,
        PATTERN0,
        PATTERN1,
        PATTERN2,
        PATTERN3,
        PATTERN4,
        PATTERN5,
        PATTERN6,
        PATTERN7,
        PATTERN8,
        PATTERN9,
        PATTERN10,
        PATTERN11,
        PATTERN12,
        PATTERN13,
        PATTERN14,
        PATTERN15);
    signal currentState: States_t;
    signal nextState: States_t;

    constant ACTIVE: std_logic := '1';

    constant HIGH_Z_LEDS : std_logic_vector(15 downto 0) := "ZZZZZZZZZZZZZZZZ";
    constant PATTERN0_LEDS : std_logic_vector(15 downto 0) := "1111111111111111";
    constant PATTERN1_LEDS : std_logic_vector(15 downto 0) := "1111111111111110";
    constant PATTERN2_LEDS : std_logic_vector(15 downto 0) := "1111111111111100";
    constant PATTERN3_LEDS : std_logic_vector(15 downto 0) := "1111111111111000";
    constant PATTERN4_LEDS : std_logic_vector(15 downto 0) := "1111111111110000";
    constant PATTERN5_LEDS : std_logic_vector(15 downto 0) := "1111111111100000";
    constant PATTERN6_LEDS : std_logic_vector(15 downto 0) := "1111111111000000";
    constant PATTERN7_LEDS : std_logic_vector(15 downto 0) := "1111111110000000";
    constant PATTERN8_LEDS : std_logic_vector(15 downto 0) := "1111111100000000";
    constant PATTERN9_LEDS : std_logic_vector(15 downto 0) := "1111111000000000";
    constant PATTERN10_LEDS : std_logic_vector(15 downto 0) := "1111110000000000";
    constant PATTERN11_LEDS : std_logic_vector(15 downto 0) := "1111100000000000";
    constant PATTERN12_LEDS : std_logic_vector(15 downto 0) := "1111000000000000";
    constant PATTERN13_LEDS : std_logic_vector(15 downto 0) := "1110000000000000";
    constant PATTERN14_LEDS : std_logic_vector(15 downto 0) := "1100000000000000";
    constant PATTERN15_LEDS : std_logic_vector(15 downto 0) := "1000000000000000";

    signal stateMachineControl: std_logic;

begin

    ------------------------------------------------------------------------------------
    -- The state machine register that keeps track of when to switch to the next state.
    ------------------------------------------------------------------------------------
    STATE_REGISTER: process(reset, clock)
        begin
        if reset = ACTIVE then
        currentState <= BLANK;
        elsif rising_edge(clock) then
        currentState <= nextState;
        end if;
    end process;

    ------------------------------------------------------------------------------------
    -- The overly complex and long winded state machine that selects different signals
    -- to reach the output. If this module is done, then the ouput is high-Z. While
    -- this module runs, output a busy signal to tell the rest of the design it busy.
    ------------------------------------------------------------------------------------
    WIN_PATTERN_SM: process(currentState, stateMachineControl, losePatternEN)
    begin
        case CurrentState is
    -------------------------------------------------------------------------------BLANK
        when BLANK =>
        leds <= HIGH_Z_LEDS;
        losePatternIsBusy <= not ACTIVE;
        if (losePatternEN = ACTIVE) then
        nextState <= PATTERN0;
        else
        nextState <= BLANK;
        end if;
    ----------------------------------------------------------------------------PATTERN0

        when PATTERN0 =>
        leds <= PATTERN0_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN1;
        else
        nextState <= PATTERN0;
        end if;
    -----------------------------------------------------------------------------PATTERN1

        when PATTERN1 =>
        leds <= PATTERN1_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= PATTERN2;
        else
        nextState <= PATTERN1;
        end if;
    -----------------------------------------------------------------------------PATTERN2

        when PATTERN2 =>
        leds <= PATTERN2_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN3;
        else
        nextState <= PATTERN2;
        end if;
    -----------------------------------------------------------------------------PATTERN3

        when PATTERN3 =>
        leds <= PATTERN3_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= PATTERN4;
        else
        nextState <= PATTERN3;
        end if;
    -----------------------------------------------------------------------------PATTERN4

        when PATTERN4 =>
        leds <= PATTERN4_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN5;
        else
        nextState <= PATTERN4;
        end if;
    -----------------------------------------------------------------------------PATTERN5

        when PATTERN5 =>
        leds <= PATTERN5_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= PATTERN6;
        else
        nextState <= PATTERN5;
        end if;
    -----------------------------------------------------------------------------PATTERN6

        when PATTERN6 =>
        leds <= PATTERN6_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN7;
        else
        nextState <= PATTERN6;
        end if;
    -----------------------------------------------------------------------------PATTERN7

        when PATTERN7 =>
        leds <= PATTERN7_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= PATTERN8;
        else
        nextState <= PATTERN7;
        end if;
    -----------------------------------------------------------------------------PATTERN8

        when PATTERN8 =>
        leds <= PATTERN8_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN9;
        else
        nextState <= PATTERN8;
        end if;
    -----------------------------------------------------------------------------PATTERN9

        when PATTERN9 =>
        leds <= PATTERN9_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= PATTERN10;
        else
        nextState <= PATTERN9;
        end if;
    -----------------------------------------------------------------------------PATTERN10

        when PATTERN10 =>
        leds <= PATTERN10_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN11;
        else
        nextState <= PATTERN10;
        end if;
    -----------------------------------------------------------------------------PATTERN11

        when PATTERN11 =>
        leds <= PATTERN11_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= PATTERN12;
        else
        nextState <= PATTERN11;
        end if;
    -----------------------------------------------------------------------------PATTERN12

        when PATTERN12 =>
        leds <= PATTERN12_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN13;
        else
        nextState <= PATTERN12;
        end if;
    -----------------------------------------------------------------------------PATTERN13

        when PATTERN13 =>
        leds <= PATTERN13_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= PATTERN14;
        else
        nextState <= PATTERN13;
        end if;
    -----------------------------------------------------------------------------PATTERN14

        when PATTERN14 =>
        leds <= PATTERN14_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = not ACTIVE) then
        nextState <= PATTERN15;
        else
        nextState <= PATTERN14;
        end if;
    -----------------------------------------------------------------------------PATTERN15

        when PATTERN15 =>
        leds <= PATTERN15_LEDS;
        losePatternIsBusy <= ACTIVE;
        if (stateMachineControl = ACTIVE) then
        nextState <= BLANK;
        else
        nextState <= PATTERN15;
        end if;
        end case;
    end process;

    DISPLAY_RATE: process(reset, clock)
        variable count: integer range 0 to BLINK_COUNT;
    begin
        if (reset = ACTIVE) then
        count := 0;
        stateMachineControl <= not ACTIVE;
        elsif (rising_edge(clock)) then
        if (count >= BLINK_COUNT) then
        count := 0;
        stateMachineControl <= not stateMachineControl;
        else
        count := count + 1;
        end if;
        end if;
    end process DISPLAY_RATE;

end LosePattern_ARCH;

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

------------------------------------------------------------------------------------
--Title: LedSegments
--Name: Nathaniel Roberts, Mitch Walker
--Date: 3/26/25
--Prof: Scott Tippens
--Desc: Bar Led Driver file
-- This file simply chooses which led on the Basys3 board will recieve the active
-- level. The inupt is a 4 bit binary number and output is 16 bit wide vector.
-- matching the position of each of the 16 leds on the Basys3 board.
------------------------------------------------------------------------------------

entity LedSegments is
    port(
        binary4Bit : in std_logic_vector(3 downto 0);
        outputMode : in std_logic;

        leds : out std_logic_vector(15 downto 0)
    );
end entity LedSegments;

architecture LedSegments_ARCH of LedSegments is

begin

    DRIVE_LEDS : process(binary4Bit, outputMode)
    begin
        if outputMode = '0' then
        leds <= (others => 'Z');
        else
        for i in 0 to 15 loop
        if to_integer(unsigned(binary4BIt)) = i then
        leds(i) <= '1';
        else
        leds(i) <= '0';
        end if;
        end loop;
        end if;
    end process;

end architecture LedSegments_ARCH;

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

------------------------------------------------------------------------------------
--Title: BCD
--Name: Nathaniel Roberts, Mitch Walker
--Date: 3/26/25
--Prof: Scott Tippens
--Desc: Binary to BCD converter file.
-- This component simply converts a 4 bit binary number into two seperate
-- 4 bit numbers to represent the Tens and ones place combinationally.
------------------------------------------------------------------------------------

entity BCD is
    port(
        binary4Bit : in std_logic_vector(3 downto 0);

        decimalOnes : out std_logic_vector(3 downto 0);
        decimalTens : out std_logic_vector(3 downto 0)
    );
end entity BCD;

architecture BCD_ARCH of BCD is
begin
    with binary4Bit select
        decimalOnes <= "0000" when "0000",
        "0001" when "0001",
        "0010" when "0010",
        "0011" when "0011",
        "0100" when "0100",
        "0101" when "0101",
        "0110" when "0110",
        "0111" when "0111",
        "1000" when "1000",
        "1001" when "1001",
        -------------------
        "0000" when "1010",
        "0001" when "1011",
        "0010" when "1100",
        "0011" when "1101",
        "0100" when "1110",
        "0101" when "1111",
        (others => '0') when others;

    with binary4Bit select
        decimalTens <= "0000" when "0000",
        "0000" when "0001",
        "0000" when "0010",
        "0000" when "0011",
        "0000" when "0100",
        "0000" when "0101",
        "0000" when "0110",
        "0000" when "0111",
        "0000" when "1000",
        "0000" when "1001",
        -------------------
        "0001" when "1010",
        "0001" when "1011",
        "0001" when "1100",
        "0001" when "1101",
        "0001" when "1110",
        "0001" when "1111",
        (others => '0') when others;
end architecture BCD_ARCH;
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

------------------------------------------------------------------------------------
--Title: Memory Game
--Name: Nathaniel Roberts, Mitch Walker
--Date: 4/23/25
--Prof: Scott Tippens
--Desc: Memory Game testbench file
-- This file uses seperate processes to find what the numerical display numbers
-- are and output the cooresponding one pulse wide switch signal
--
-- The testbench can be configured for any timing range based on the generic
-- parameters.
------------------------------------------------------------------------------------

entity MemoryGameTB is
end entity;

architecture Behavioral of MemoryGameTB is

    ------------------------------------------------------------------------------------
    --Unit under test definition
    ------------------------------------------------------------------------------------
    component MemoryGame
        generic(
        MAX_COUNT_SCALER : integer;
        SCALE_AMOUNT : integer;
        MAX_TOGGLE_COUNT : integer;
        BLINK_COUNT : integer
        );
        port(
        switches : in std_logic_vector(15 downto 0);
        start : in std_logic;
        clock : in std_logic;
        reset : in std_logic;
        leds : out std_logic_vector(15 downto 0);
        outputScore : out std_logic_vector(7 downto 0);
        blanks : out std_logic_vector(3 downto 0)
        );
    end component MemoryGame;

    ------------------------------------------------------------------------------------
    --testbench signals
    ------------------------------------------------------------------------------------
    signal switches : std_logic_vector(15 downto 0) := (others => '0');
    signal start : std_logic;
    signal clock : std_logic;
    signal reset : std_logic;
    signal leds : std_logic_vector(15 downto 0);
    signal blanks : std_logic_vector(3 downto 0);
    signal outputScore : std_logic_vector(7 downto 0);

    constant CLOCK_PERIOD : time := 10 ns;
    constant MAX_COUNT_SCALER : integer := 0;
    constant SCALE_AMOUNT : integer := 50;
    constant MAX_TOGGLE_COUNT : integer := 100;
    constant BLINK_COUNT : integer := 25;

    type testVector_t is array(0 to 4) of integer;
    signal number_reg : testVector_t;

    signal load_number_regEN : std_logic := '0';
    signal load_number_reg_completeEN : std_logic := '0';

    --MAX_TOGGLE_COUNT * CLOCK_PERIOD = 1000
    constant getNumberDelay : time := 1000 ns;
    --BLINK_COUNT * COCK_PERIOD = 250
    --25 * 10 = 250
    constant patternDelay : time := 250 ns;

begin

    ------------------------------------------------------------------------------------
    --Design instantiation
    ------------------------------------------------------------------------------------
    UUT : MemoryGame
    generic map(
        MAX_COUNT_SCALER => MAX_COUNT_SCALER,
        SCALE_AMOUNT => SCALE_AMOUNT,
        MAX_TOGGLE_COUNT => MAX_TOGGLE_COUNT,
        BLINK_COUNT => BLINK_COUNT
    )
    port map(
        switches => switches,
        start => start,
        clock => clock,
        reset => reset,

        ------------------outputs
        leds => leds,
        outputScore => outputScore,
        blanks => blanks
    );

    ------------------------------------------------------------------------------------
    -- Clock generator
    ------------------------------------------------------------------------------------
    CLOCK_GEN : process
    begin
        clock <= '0';
        wait for (CLOCK_PERIOD / 2);
        clock <= '1';
        wait for (CLOCK_PERIOD / 2);
    end process;

    ------------------------------------------------------------------------------------
    -- Reset button generator
    ------------------------------------------------------------------------------------
    RESET_GEN : process
    begin
        wait until rising_edge(clock);
        wait until rising_edge(clock);
        reset <= '1';
        wait until rising_edge(clock);
        reset <= '0';
        wait;
    end process;

    ------------------------------------------------------------------------------------
    -- This process can scan the output of the switches and assign those values into
    -- an array of integers.
    ------------------------------------------------------------------------------------
    TEST_REGISTER : process
    begin
        wait until rising_edge(load_number_regEN);
        wait for getNumberDelay;
        for k in 0 to 4 loop
        for i in 0 to 15 loop
        if leds(i) = '1' then
        number_reg(k) <= i;
        end if;
        end loop;
        wait for getNumberDelay; --dont start i loop until next number pops up
        wait for getNumberDelay;
        end loop;

        load_number_reg_completeEN <= '1';
        wait until rising_edge(clock);
        load_number_reg_completeEN <= '0';
        wait until rising_edge(clock);

    end process;

    ------------------------------------------------------------------------------------
    -- Main stimulus process with necessary timing procedures
    ------------------------------------------------------------------------------------
    STIMULUS : process
    begin
        wait for 500 ns;

        start <= '1'; --start button pressed
        wait until rising_edge(clock);
        start <= '0';
        wait until rising_edge(clock);

        --first round-------------------------------------------------------------------
        load_number_regEN <= '1'; --trigger the TEST_REGISTER process
        wait until rising_edge(clock); --to load numbers as the numbers are brought up.
        load_number_regEN <= '0';
        wait until rising_edge(clock);

        wait until rising_edge(load_number_reg_completeEN); --wait for the loop to be done

        switches(number_reg(0)) <= '1'; --plug in numbers
        wait until rising_edge(clock);
        switches(number_reg(0)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(1)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(1)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(2)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(2)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(3)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(3)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(4)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(4)) <= '0';
        wait until rising_edge(clock);

        --second round------------------------------------------------------------------
        wait for 2000 ns;

        load_number_regEN <= '1'; --trigger the TEST_REGISTER process
        wait until rising_edge(clock); --to load numbers as the numbers are brought up.
        load_number_regEN <= '0';
        wait until rising_edge(clock);

        wait until rising_edge(load_number_reg_completeEN); --wait for the loop to be done

        switches(number_reg(0)) <= '1'; --plug in numbers
        wait until rising_edge(clock);
        switches(number_reg(0)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(1)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(1)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(2)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(2)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(3)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(3)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(4)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(4)) <= '0';
        wait until rising_edge(clock);

        --third round--------------------------------------------------------------------
        wait for 1100 ns;

        load_number_regEN <= '1'; --trigger the TEST_REGISTER process
        wait until rising_edge(clock); --to load numbers as the numbers are brought up.
        load_number_regEN <= '0';
        wait until rising_edge(clock);

        wait until rising_edge(load_number_reg_completeEN); --wait for the loop to be done

        switches(number_reg(0)) <= '1'; --plug in numbers
        wait until rising_edge(clock);
        switches(number_reg(0)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(1)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(1)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(2)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(2)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(3)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(3)) <= '0';
        wait until rising_edge(clock);

        switches(number_reg(4)) <= '1';
        wait until rising_edge(clock);
        switches(number_reg(4)) <= '0';
        wait until rising_edge(clock);
        wait;
    end process;

end architecture Behavioral ;

library IEEE;
use IEEE.std_logic_1164.all;
use IEEE.numeric_std.all;

------------------------------------------------------------------------------------
--Title: MemoryGame
--Name: Nathaniel Roberts, Mitch Walker
--Date: 4/23/25
--Prof: Scott Tippens
--Desc: Wrapper file
--
-- This Top wrapper uses 3 generate statements for the array of 16 switches
-- The first in the signal chain is a SynchronizerChain component to handle
-- meta stability. The second component debounces the switches and the final
-- component pulsees each switch.
--
-- The same hardware signal chain exists for the start button.
--
------------------------------------------------------------------------------------

entity MemoryGame_Basys3 is
    generic(
        NUM_OF_SWITCHES : integer := 16;
        CHAIN_SIZE : integer := 2;
        DELAY_COUNT : integer := 10_000_000 --10ms on a 100MHz clock = 1M
        );
    port(
        sw : in std_logic_vector(NUM_OF_SWITCHES-1 downto 0);
        btnC : in std_logic; --start/restart button
        btnD : in std_logic; --reset/blanks the screens
        clk : in std_logic;

        led : out std_logic_vector(15 downto 0);
        an : out std_logic_vector(3 downto 0);
        seg : out std_logic_vector(6 downto 0)
    );
end entity;

architecture MemoryGame_Basys3_ARCH of MemoryGame_Basys3 is

    ------------------------------------------------------------------------------------
    --component definitions
    ------------------------------------------------------------------------------------
    component MemoryGame
    generic(
    MAX_COUNT_SCALER : integer;
    SCALE_AMOUNT : integer;
    MAX_TOGGLE_COUNT : integer;
    BLINK_COUNT : integer
        );
    port(
    switches : in std_logic_vector(15 downto 0);
    start : in std_logic;
    clock : in std_logic;
    reset : in std_logic;
    leds : out std_logic_vector(15 downto 0);
    outputScore : out std_logic_vector(7 downto 0);
    blanks : out std_logic_vector(3 downto 0)
    );
    end component MemoryGame;

    component SevenSegmentDriver is
        port(
        reset: in std_logic;
        clock: in std_logic;

        digit3: in std_logic_vector(3 downto 0); --leftmost digit
        digit2: in std_logic_vector(3 downto 0); --2nd from left digit
        digit1: in std_logic_vector(3 downto 0); --3rd from left digit
        digit0: in std_logic_vector(3 downto 0); --rightmost digit

        blank3: in std_logic; --leftmost digit
        blank2: in std_logic; --2nd from left digit
        blank1: in std_logic; --3rd from left digit
        blank0: in std_logic; --rightmost digit

        sevenSegs: out std_logic_vector(6 downto 0); --MSB=g, LSB=a
        anodes: out std_logic_vector(3 downto 0) --MSB=leftmost digit
        );
    end component;

    component SynchronizerChain is
        generic (CHAIN_SIZE: positive);
        port (
        reset: in std_logic;
        clock: in std_logic;
        asyncIn: in std_logic;
        syncOut: out std_logic
        );
    end component;

    component Debouncer is
        generic( DELAY_COUNT : positive);
        port(
        bitIn : in std_logic;
        clock : in std_logic;
        reset : in std_logic;

        debouncedOut : out std_logic
        );
    end component;

    component LevelDetector is
        port (
        reset: in std_logic;
        clock: in std_logic;
        trigger: in std_logic;
        pulseOut: out std_logic
        );
    end component;

    -------------------------------------------------------------------------------
    -- synchronized 16 bit wide vector of switches
    -- vector is fed to a debouncer then finally a pulse controller
    -------------------------------------------------------------------------------
    signal synchedSwitches : std_logic_vector(NUM_OF_SWITCHES-1 downto 0);
    signal debouncedSwitches : std_logic_vector(NUM_OF_SWITCHES-1 downto 0);
    signal pulsedSwitches : std_logic_vector(NUM_OF_SWITCHES-1 downto 0);

    -------------------------------------------------------------------------------
    -- synchronised start button signal path
    -------------------------------------------------------------------------------
    signal startButtonSync : std_logic;
    signal startButtonDebounced : std_logic;
    signal startButtonPulsed : std_logic;

    -------------------------------------------------------------------------------
    --signals for SevenSegmentDriver component
    -------------------------------------------------------------------------------
    signal blanks : std_logic_vector(3 downto 0);
    signal outputScore : std_logic_vector(7 downto 0);

    begin------------------------------------------------------------------------------begin

    ------------------------------------------------------------------------------------
    --component insantiations
    ------------------------------------------------------------------------------------

    MEMORY_GAME : component MemoryGame
        generic map(
        MAX_COUNT_SCALER => 90_000_000,
        SCALE_AMOUNT => 15_000_000,
        MAX_TOGGLE_COUNT => 100_000_000,
        BLINK_COUNT => 25_000_000
        )
    port map(
        switches => pulsedSwitches,

        start => startButtonPulsed,

        clock => clk,
        reset => btnD,

        leds => led,

        outputScore => outputScore,

        blanks => blanks
    );

    SEGMENT_DRIVER : component SevenSegmentDriver port map(
        reset => btnD,
        clock => clk,

        digit3 => outputScore(7 downto 4),
        digit2 => outputScore(3 downto 0),
        digit1 => "0000",
        digit0 => "0000",

        blank3 => blanks(3),
        blank2 => blanks(2),
        blank1 => blanks(1),
        blank0 => blanks(0),

        sevenSegs => seg,
        anodes => an
    );

    ------------------------------------------------------------------------------------
    -- generate chain of 2 flip-flops for each vector switch element
    ------------------------------------------------------------------------------------
    SYNC : for i in 0 to NUM_OF_SWITCHES-1 generate
        SYNC_X : component SynchronizerChain
        generic map(
        CHAIN_SIZE => CHAIN_SIZE
        )
        port map(
        reset => btnD,
        clock => clk,
        asyncIn => sw(i),
        syncOut => synchedSwitches(i) --all switches now clock synced
        );
    end generate;

    ------------------------------------------------------------------------------------
    -- generate debounce control for each vector switch element
    ------------------------------------------------------------------------------------
    DEBOUNCE : for i in 0 to NUM_OF_SWITCHES-1 generate
        DEBOUNCE_X : component Debouncer
        generic map(
        DELAY_COUNT => DELAY_COUNT
        )
        port map(
        bitIn => synchedSwitches(i),
        clock => clk,
        reset => btnD,
        debouncedOut => debouncedSwitches(i) --all switches now debounced
        );
    end generate;

    ------------------------------------------------------------------------------------
    -- make each switch pulse, once per activation, reset once the switch is down
    ------------------------------------------------------------------------------------
    PULSE : for i in 0 to NUM_OF_SWITCHES-1 generate
        PULSE_X : component LevelDetector
        port map(
        reset => btnD,
        clock => clk,
        trigger => debouncedSwitches(i),
        pulseOut => pulsedSwitches(i) --all switches now pulse controlled
        );
    end generate;

    ------------------------------------------------------------------------------------
    -- The following 3 components synchronize, debounce and pulse the start button.
    ------------------------------------------------------------------------------------
    START_BUTTON_SYNC : SynchronizerChain
        generic map(
        CHAIN_SIZE => CHAIN_SIZE
        )
        port map(
        reset => btnD,
        clock => clk,
        asyncIn => btnC,
        syncOut => startButtonSync --start button is now synced
    );

    START_BUTTON_DEBOUNCE : component Debouncer
        generic map(
        DELAY_COUNT => DELAY_COUNT
        )
        port map(
        bitIn => startButtonSync,
        clock => clk,
        reset => btnD,
        debouncedOut => startButtonDebounced --start button is now debounced
    );

    START_BUTTON_PULSE : LevelDetector
        port map(
        reset => btnD,
        clock => clk,
        trigger => startButtonDebounced,
        pulseOut => startButtonPulsed --start button is now pulsed
    );

end MemoryGame_Basys3_ARCH;

library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;

------------------------------------------------------------------------------------
--Title: Debouncer.vhd
--Name: Nathaniel Roberts, Mitch Walker
--Date: 4/23/25
--Prof: Scott Tippens
--Desc: Counter based denouncing component.
-- This component checks to see if the user input has remained in its position
-- for the full duration of the count. If that signal input is different than the
-- output and the counter has also not yet reached its terminal value, then the
-- input is not yet stable and the component keeps the signal from reflecting to
-- the output.
------------------------------------------------------------------------------------

entity Debouncer is
    generic(
        DELAY_COUNT : positive
    );
    port(
        bitIn : in std_logic;
        clock : in std_logic;
        reset : in std_logic;

        debouncedOut : out std_logic
    );
end entity Debouncer;

architecture Debouncer_ARCH of Debouncer is
    signal counter : integer range 0 to DELAY_COUNT;
    signal bitReg : std_logic;
begin
    SCAN_INPUT : process(clock, reset)
    begin
        if reset = '1' then
        counter <= 0;
        elsif rising_edge(clock) then
        if bitIn /= bitReg and counter < DELAY_COUNT then
        counter <= counter + 1;
        elsif counter >= DELAY_COUNT then
        bitReg <= bitIn;
        counter <= 0;
        else
        counter <= 0;
        end if;
        end if;
    end process;
    debouncedOut <= bitReg;
end architecture Debouncer_ARCH;